## Slide 1: GDRM methodology: Progress update
Prof Thokozani Kanyerere (UWC) plus UWC Research Team
This is a Team work. We need a reflective discussion on presentation
Is it feasible/practical? Will the product help us as practitioners or regulators? Where can we improve still?
June 2023 Deliverable

## Slide 2: Outline of the presentation
Variables for GRDM Studies: 09:30-10:15] 45 Minutes]
GRDM Resource Unit Delineation [Aquifer Delineation]: 12:00-12:45 [45 Minutes]
GRDM Classification: Status Quo: Assessment for Quantity 10:45-11:30 [45Minutes]:
GRDM Classification: Status Quo: Assessment for Quality 10:45-11:30 [30 Minutes]

## Slide 3
Modus Operandi
We are here to show what we have been working on for you to see whether or not is it feasible and whether or not the product will be useful for your day-to-day work as practitioners and regulators and scientists
This workshop is a reflective workshop on the practicality of the tasks that we have been doing
Over the last decade, new knowledge and new thinking have become available regarding groundwater systems that may not have been accounted for in the 2013 GRDM methodology, so the need for the update

## Slide 4: Why are we here this week?
Specific objectives for the project are as follows:
1) To update the GRDM methodology for classification, Reserve determination, and setting of RQOs for groundwater resources,
2) To improve the GRDM software with user-friendly features and its functionality,
3) To provide theoretical training on the GRDM methodology, practical training on field data collection, and practical demonstration on the application of the GRDM software. We aim to provide tasks to improve the computation/analysis of data for GW protection and for the uptake of improved knowledge and practical skills.
To improve GRDM methodology and its associated software to standardize the approach used in all GRDM studies and to improve knowledge and practical skills necessary for GRDM

## Slide 5: The focus of the workshop
The project focuses only on the aspects that have been identified as needing improvements. Thus, we are not updating the entire GRDM Manual as you know it
The identified key focus areas that required improvement were grouped into six (6) key focus areas which are 1) key parameters, 2) water resource classification, 3) Reserve determination, 4) determination of RQOs, 5) the GRDM software, and 6) GRDM implementation

## Slide 6: GDRM methodology: Progress update
Variables for GRDM Studies: 09:30-10:15] 45 Minutes

## Slide 7: 1. Recharge
Recharge-related concepts require review:
Potential Vs actual recharge
Local Vs regional recharge
Annual Vs seasonal
Vertical Vs horizontal recharge
Focussed Vs diffuse recharge
Lithological Vs water table-based aquifer type
Local versus catchment scale

## Slide 8
Zone | Method | Limitation | Applicability |  |  | Rating |  | 
 |  |  | Flux mm/year | Area (km2) | Time (years) | Acc. | Ease | Cost
SW | Baseflow | Emphermal rivers [NPR system] | 400-4000 (0.1-1000) | 10-4-1300 (10-1000) | 0.3-50 (1-100) | 2 | 2 | 1-2
 | CWB | Inaccurate flow measurements | 100-5000 | 10-3-10 | 1d-1yr | 2-3 | 2 | 3
 | WB | Emphermal rivers [NPR system] | 1-400 | 10-1-5×105 | 1d-10yr | 2 | 2-3 | 3
Unsaturated | Lysimeter | Surface runoff | 1-500 | 0.1-30m2 | 0.1-6 | 1-2 | 3 | 3
 | UFM | Poor known relationship between hydraulic conductivity- moisture | 20-500 | 0.1-1m2 | 0.1-400 | 3 | 2 | 2
 | ZFP | Subsurface heterogeneity, periods of high infiltration | 30-500 | 0.1-1m2 | 0.1-6 | 3 | 2 | 2
 | CMB | Long term atmospheric deposition unknown | 0.1-300 (0.6-300) | 0.1-1m2 | 5-10000 | 2 | 1 | 1
 | Historical | Poorly known porosity; present 3H levels almost undetectable | 10-50 (10-80) | 0.1-1m2 | 1.5-50 | 2-3 | 2-3 | 3
Saturated - Unsaturated | CRD | Deep (multi-layer) aquifers, sensitive to Specific yield (Sy) | (0.1-1000) | (1-1000) | (0.1-20) | 1-2 | 1-2 | 1
 | EARTH | Poorly known Sy | (1-80) | (1-10m2) | (1-5) | 1-2 | 2 | 1
 | WTF | In/outflow Sy usually unknown | 5-500 | 5×10-5>10-3 | 0.1-5 | 2 | 1 | 1
 | CMB | Long term atmospheric deposition unknown | 0.1-500 | 2×10-6– >10-2 | 5->10000 | 2 | 1 | 1
Saturated | GM | Time consuming, poorly known transmissivity, sensitive to boundary Conditions | (0.1-1000) | (10-6-109) | (1d–20yr) | 2 | 3 | 2-3
 | SVF | Flow-through region; multi layered aquifer | (0.1-1000) | (1-1000) | (0.1-20) | 1-2 | 1-2 | 1
 | EV-SF | Confined aquifer | (0.1-1000) | (1-100) | (1-100) | 1-2 | 1-2 | 1-2
 | GD | 14C,3H/3He, CFC: poorly known porosity / correlation of dead carbon contribution | 14C: 1-100 3H/3He, CFC: 30- 1000 | 14C, 3H/He3, CFC: 2*10-6->10-3 | 14C: 200-200000 3H/He3, CFC: 2- 40 | 3 | 2 | 3
Recharge value for potential recharge ad actual recharge has implications when making a decision about water allocation and water protection
We might allocate what is not actually available in the aquifer system
We might be making plans to protect the water that is not available in the aquifer system
Understand hydrological zone then apply recommended methods [Scanlon et al 2002 in Xu & Beekman 2003]

## Slide 9
Methods that are recommended for the saturated zone
are suitable for estimating Local Vs regional recharge

## Slide 11
Aquifers are classified as unconfined or confined depending on the presence or absence of a water table, while a leaky aquifer represents a combination of the two types. Confined aquifers are also called artesian/pressured aquifers. Are TMG confined or unconfined aquifers?

## Slide 13
UWC 1
UWC 2
UWC 3
UWC 4
UWC 5
UWC 6
11m
30m
37m
22m
105m
83m
6m
12m
6m
3m
12m
12m
Primary Cape Flats Sand Stone Aquifer
Secondary Malmasbury Fractured Aquifer
Screen
PVC
Casting
Cross Section of UWC Borehole Test Site
6m
61m
19m
29m
16m
3m

## Slide 14
UWC 1
UWC 2
UWC 3
UWC 4
UWC 5
UWC 6
LITHO- LOGS OF MONITORING WELL AT UWC TEST SITE
Sand and Peat
Clay and Peat
Clay
Peat
Malmesbury Shale
10m
20m
30m
40m
50m
60m
70m
80m
90m
100m

## Slide 15
Recharge value for local recharge and regional recharge is not clarified especially where two water table-based aquifer systems co-exist.
For example, coastal aquifer systems such as Cape Flat Aquifer System which has an unconfined and confined aquifer system, are recharged differently.
Boreholes A and B may show no water and hence groundwater allocation can be denied while the user or farmer will insist with evidence that his borehole C has water all the time because his borehole is drilled into a deeper confined system which is recharged with water away from the location of tha borehole C.
Such a situation renders practitioners less competent compared with some lived-experienced groundwater users

## Slide 16: Take home message
Aquifer-focus so all aquifer should be delineated
Focus on local [Unconfined] and regional [Confined]recharge
Improve knowledge of BHs in Unconfined & confined aquifers
GW Planning according to aquifer types [Dual layered system]
GW Assessment according to aquifer types [Dual layered system]
GW Protection according to aquifer types [Dual layered system]
GW Monitoring according to aquifer types [Dual layered system]
GW Allocation/Abstraction/Use according to aquifer types [Dual layered system]
GW Governance according to aquifer types [Dual layered system]
For example, we need to know the number of BHs in unconfined and confined aquifer systems and monitor levels and quality according. Such information is critical for various uses than the current generic or generalization of GW information

## Slide 17: Calculations will be demonstrated during the practical session
Recharge in unconfined and confined aquifers are presented in case studies for Upper Berg[G10A] and Heuningnes [G50]:

## Slide 18: 2. Groundwater Contribution to Baseflow
Currently, we use baseflow instead of estimating groundwater contribution to baseflow. Baseflow is made of up water from various sources and one of the sources is groundwater. In this study, we present how we estimated groundwater contribution to base flow
GRDM studies should always estimate groundwater contribution to baseflow using existing methods to provide a better estimation of groundwater roles in ecological ecosystem sustainability.
The equation for calculating groundwater contribution to baseflow is provided for discussion, testing/piloting and refinement then adoption
During the session when we determine the reserve for GRDM, we discuss and agree on whether or not we should retain the baseflow on the Template for Reserve Determination table

## Slide 19: Groundwater contribution to baseflow
Hall (1968) defines baseflow as the portion that is contributed to the stream by delayed sources (unsaturated zone water, lakes, perched stream) and groundwater. Baseflow definition as the lowest discharge of the stream in the dry season and not generalized as groundwater contribution to surface water must be understood. Baseflow has multiple sources which include groundwater i.e. groundwater contribution to surface water is not baseflow but a portion of baseflow.

## Slide 20
Groundwater contribution to baseflow is affected by the assumption, which states that the volume of groundwater retained in storage functions as a buffer during dry periods. Suggesting that, that volume could contribute to baseflow during the dry season. But to conclude this, an understanding of hydrogeological characteristics is necessary, hence the suggestion of thorough testing of these assumptions with groundwater contribution to baseflow method to be sure of their applicability in various hydrogeological settings. WRC Study 2013 has details about the use of baseflow.

## Slide 21
In the current methods, we consider the total population in the study area as reliant on groundwater leading into overestimation of groundwater required for basic human needs
In the proposed method update, we only considered the population that uses/depend on groundwater. We called such a population, Groundwater-dependent population. We obtained such data from the WARMS database for the registered groundwater users. Such information is likely to underreport groundwater users due to schedule one users, ELW users, and CBA users for disclosing, among others. Working closely with engaging stakeholders, municipalities, and DWS Regional Office, Catchment Management Agencies would improve knowledge on groundwater users.
Using groundwater-dependent populations would improve the fair allocation of groundwater for basic human needs and such an approach would be more accurate. However, there is a need to explore a method that would enable all groundwater users to disclose their groundwater use such as Verification and validation techniques among others.
3. Basic Human Needs

## Slide 22
The existing methodology uses the above equation to calculate Basic Human Needs Reserve [BHN].In the current study, we use groundwater dependant populations [GDP] only i.e. only the population that depends on or uses groundwater is considered. We are getting this data from municipalities on abstraction volumes from their local groundwater schemes. The reality is that not everyone in a catchment or study area uses or depends on groundwater hence the focus GDP only.
There will be an icon in the software for GDP. This is the update on the current methodology

## Slide 23
4. Groundwater Quality Variables
In the current methods, we heavily rely on Electrical Conductivity (EC) as an indicator of water quality, especially in Step 1 of the water resources classification for status quo. This approach overshadows the identification of areas experiencing water quality challenges linked to other variables such as Magnesium, Sulphate among others
In this study we demonstrate how we used Groundwater Quality Index provide a comprehensive assessment of groundwater quality status in the study area. We recommend to obtain more water quality data through ground-truthing and requests from private landowners or water users among others in addition to the existing water quality data from national databases
We recommends that more data on several water quality variables is likely to provide a comprehensive assessment of groundwater quality status in the study area. The use of EC plus more water quality variables is recommended where data are available [Precautionary Principle].

## Slide 24: GDRM methodology: Progress update
GRDM Resource Unit Delineation [Aquifer Delineation]: [45 Minutes]

## Slide 25
The key outcome of this step is a map demarcating UAs, each of which is to be classified, a Reserve assessment undertaken and Resource Quality Objectives (RQOs) set. In most instances, it is assumed that the UA is the quaternary catchment. This might not always be the case. The UAs are decided based on geohydrological, hydrological and ecological criteria considering the significance of groundwater among others.
Step 1: Delineate the units of analysis (UA) and describe the status quo of the water resource(s)
For the GRDM of this project, the key outcome of this step is a delineated aquifer where a Reserve assessment is undertaken and Resource Quality Objectives (RQOs) are set. In this current project, this delineated aquifer is a dual-layered delineated aquifer system [Unconfined and confined Aquifer system]. Step 1: Shapefiles of the quaternary catchment are accessed; Step 2: The aquifer is delineated with all the steps followed producing the final product as a delineated aquifer; Step 3; Overlay of the quaternary catchment on a delineated aquifer. The delineated aquifer was carried out based on geological and geohydrological information including boreholes.

## Slide 27
The existing GRDM methodology, according to Dennis (pers com), does account for aquifer boundaries, however most of the information is sitting / provided at quaternary scale which do not directly coincide [WRC 2013].
iii) Delineation of the units of analysis [Groundwater Resource Units]
GRDM studies should deal with the aquifer delineation. Establishing how to scale up and down between aquifer and quaternary catchment delineation is one strategy that could be used.
Here we provide what we did to delineate the aquifer system because we believe that having a clear approach to working with aquifer boundaries and quaternary scale would allow for standardization of the GRDM methodology for easy implementation of outcomes emanating from GRDM studies.

## Slide 34
We can estimate recharge for confined and unconfined aquifer systems; we can monitor each system; we can allocate water from each system if we know the number of boreholes tapping in each system after aquifer delineation

## Slide 35
The Figure above shows lithological cross-section of the selected boreholes in the Heuningnes Catchment. Such information on the map provided data on the existence of unconfined and confined aquifer systems in the catchment for calculating the Groundwater Stress Index and Environmental Stress Index and for setting Reserve and RQOs. This report recommends that groundwater allocation, monitoring and protection must be done for aquifer scale

## Slide 36
The Figure above shows lithological cross-section of the selected boreholes in the Heuningnes Catchment. Such information on the map provided data on the existence of unconfined and confined aquifer systems in the catchment for calculating the Groundwater Stress Index and Environmental Stress Index and for setting Reserve and RQOs. This report recommends that groundwater allocation, monitoring and protection must be done for the aquifer scale.

## Slide 37: Practical session
During a practical session, our team will showcase the processes that were followed for aquifer delineation

## Slide 38: GDRM methodology: Progress update
GRDM Classification: Status Quo: Assessment for Quantity [45Minutes]

## Slide 39
Stress Index linked to groundwater use and Recharge is calculated to identify stressed areas. Groundwater use is calculated from Reserve, ie. Authorized Abstractions in WARMS. The General Stress Index overshadows areas that are still or not currently sustaining ecological ecosystems through the maintenance of EWR_MLF. For example, the general Stress Index may indicate that a certain area is not stressed at all, whereas when a Stress Index specific to the environmental requirements estimated using the relationship between “groundwater contribution to baseflow” and Ecological Water Requirements” indicates that the very same area is able to meet the requirements of the ecological ecosystem
In addition to the Stress Index calculated using “Groundwater Use” and “Recharge” it is recommended to also Calculate Stress Index linked to the environmental requirements using “Ecological Water Requirements” divided by “Groundwater Contribution to Baseflow”
Having an additional Stress Index linked specifically to Environmental Requirements provides additional information on groundwater-dependent ecosystems and their sustainability

## Slide 40
Aquifer Stress Index for groundwater use
The Aquifer Stress Index (SI) for an assessment area is defined as follows:
= 5,72%
Based on a guide for determining stress levels in a groundwater unit (Table in report), the Berg catchment with a stress index (SI) of 5,72 % falls under class I where groundwater is minimally used and therefore not stressed. This implies that there is enough groundwater to be allocated to users as the used volumes are less than the water coming into the catchment.
GRDM Classification: Status Quo: Assessment for Quantity

## Slide 41
The estimated groundwater contribution to baseflow from the confined aquifer system before and after the dam was 0.051942 m3/s and 0.399244 m3/s respectively. The addition of this two groundwater contribution to baseflow estimates produced the total groundwater contribution to baseflow from the confined aquifer system of the Upper Berg catchment which was 0.451186 m3/s. The total groundwater contribution to baseflow for the year 2022 was converted from m3/s to m3/a which was 14228601.7 m3/a (14.229 Mm3/a). The Ecological Water Requirements for Maintenance Low Flows for 2022 was 2.556 Mm3/a (WARMS).
=
GRDM Classification: Status Quo: Assessment for Quantity

## Slide 42
Stress index for confined aquifer in Heuningnes Catchment (%)
=
where
gwUse = Current groundwater use
Recharge = Recharge (as a volume)
=
= 12.57 %
Stress index for unconfined aquifer in Heuningnes Catchment (%)
SI [%] =
where
gwUse = Current groundwater use
Recharge = Recharge (as a volume)
=
= 0.68 %
GRDM Classification: Status Quo: Assessment for Quantity [Stress Index for GW availability

## Slide 43
Groundwater contribution to baseflow by the confined aquifer system of the G50B quaternary catchment of the Heuningnes catchment in 2020 = 2.5368 Mm3/a
=
This index indicates that groundwater from the confined aquifer system of the GB50 sustains the ecosystem in the area.

## Slide 44: Practical session
During a practical session, our team will showcase the processes that were followed for calculating Stress Index for confined and unconfined aquifers systems [Data must be kept according to the aquifer system]

## Slide 45: GDRM methodology: Progress update
GRDM Classification: Status Quo: Assessment for Quality [30 Minutes]

## Slide 46: Using groundwater quality index rather than EC as a parameter of water quality status
ii) Use of Electrical Conductivity (EC) as a general groundwater quality indicator
Electrical Conductivity (EC) as a general groundwater quality indicator. Challenges related to this are highlighted above [Section 1: Parameters]
Use EC under exceptional circumstances when water quality data seem to be unavailable [Precautionary Principle]
Use of other water quality parameters would provide a better understanding of water quality problems associated with other water quality parameters.

## Slide 47
The classification of water quality, based on its water quality index (WQI) after Brown et al. (1972); Chatterjee and Raziuddin (2002) and Shankar and Kawo (2019) have been considered here in this study for further reference which is mentioned in Table below
The above will be refined after calculations are compared with methods in a recent publication on GW Index [Nzama et al 2021] i.e. context specific.

## Slide 48
GWQ index based on the background condition of the aquifer: Upper Berg

## Slide 49
GWQ index based on the background condition of the aquifer: Upper Berg

## Slide 50
GWQ index based on background condition of unconfined aquifer system: Heuningnes

## Slide 51
GWQ index based on the water quality standards for drinking water Heuningnes [Salinity]

## Slide 52
GWQ index based on the background condition of the confined aquifer system, Heuningnes

## Slide 53
GWQ index based on the background condition of the confined aquifer system, Heuningnes

## Slide 54: Practical session
During a practical session, our team will showcase the processes that were followed for calculating GWQ Index and the number of parameters that were considered

## Slide 55: GDRM methodology: Progress update
GRDM Classification: Aquifer Delineation: Practical session: 13:30-14:15 [45 Minutes]:
Data sources data type and process[Step-by-step]

## Slide 56: Demonstration of data sources, data type, step-by-step
Discussion for input on the aquifer delineation [Feasibility, implication and application]

## Slide 57: GDRM methodology: Progress update
GRDM Reserve: Determining Quantity of Reserve: Practical session: 14:15-15:00 [45 Minutes]: The New Template

## Slide 58
Old Template for Quantification of Reserve: Quantity

## Slide 60
Catch | Delineated |  | Area (km2) |  | Recharge |  | Population |  | Baseflow |  | GWC_BF | MLF_EWR | BHN Reserve |  | TOTAL Reserve
 | Aquifer |  |  |  | (Mm3/a) |  |  |  | (Mm3/a) |  |  | (Mm3/a) | (Mm3/a) |  | 
 | Unconf | Confin | Unconf | Confin | Unconf | Conf | GW_Pop | Gn_Pop | Unconf | Conf |  |  | Unconf | Conf | 
 | ü | ü | 1500 | 1500 | 68,335 | 68,34 | 110 | 166825 |  | 14,229 |  | 2,556 | 18,1373 | 18,14 | 
G10A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Discussion for input on the quantity component of the reserve [Additions & substations]

## Slide 61
NB* Recharge and Baseflow values are estimated from research work and where not available, the DWS database is consulted
NB**Population data were obtained from the Population Census database and WARMS. Such data were not verified. Data on the groundwater Dependant population were taken from the WARMS database for the delineated aquifer system. Such datasets assume that the population that is registered for water use is the population that depends on groundwater. Given the issues of schedule and existing lawful water use along the validation and verification process, such datasets require precautionary principles during the interpretation

## Slide 62: GDRM methodology: Progress update
GRDM Reserve: Determining Quality of Reserve: Practical session: 14:15-15:00 [45 Minutes]:
The New Template

## Slide 63
The Old Template for a quality component of the Reserve

## Slide 64
Parameter | Ambient Ground Water Quality1) |  | Basic Human Needs Reserve2) | Ground Water Quality Reserve3) | 
 | Unconfined | Confined |  | Unconfined | Confined
Calcium (mg/L) | 8.7 | 5.6 | ≤150 | 9.57 | 6.16
Magnesium (mg/L) | 11,00 | 7.324 | ≤70 | 12.1 | 8.0564
Sodium (mg/L) | 82.417 | 58.5 | ≤200 | 90.6587 | 64.35
Chloride (mg/L) | 14.299 | 118.2925 | ≤300 | 15.7289 | 130.12175
Sulphate (mg/L) | 20.86 | 15.9145 | ≤500 | 22.946 | 17.50595
Nitrate (mg/L) | 0.153 | 0.211 | ≤11 | 0.1683 | 0.2321
Fluoride (mg/L) | 0.05 | 0.05 | ≤1.5 | 0.055 | 0.055
pH | 6.49 | 6.37 | 5 – 9.7 | 5.84 - 7.14 | 5.733-7.007
Electrical Conductivity | 68.8 | 51.2 | ≤170 | 75.68 | 56.32
Under these circumstances, site-specific data should be obtained and used to determine more representative local ambient groundwater quality conditions at the site. This Chief Directorate should be notified of such incidences, so as to revise the Reserve accordingly. For example, Iron, Manganese, and pathogens among others.
Heuningnes: Quality Reserve
The New Template for a quality component of the Reserve

## Slide 65
Parameter | Ambient Groundwater Quality |  | Basic Human Needs Reserve2) | Groundwater Quality Reserve | 
 | Unconfined | Confined |  | Unconfined | Confined
Calcium (mg/L) | 7,857 | 7,86 | <150 | 8,64 | 8,6427
Magnesium (mg/L) | 1,7717 | 1,77 | <100 | 1,95 | 1,94887
Sodium (mg/L) | 12,9 | 12,90 | <200 | 14,19 | 14,19
Chloride (mg/L) | 18,3 | 18,30 | <200 | 20,13 | 20,13
Sulphate (mg/L) | 1,9 | 1,90 | <400 | 2,09 | 2,09
Nitrate (mg/L) | 0,3645 | 0,36 | <10 | 0,40 | 0,40095
Fluoride (mg/L) | 0,2645 | 0,26 | <1,0 | 0,29 | 0,29095
pH | 7,386 | 7,39 | 5.0 – 9.5 | 6.65-8.12 | 6.65-8.12
Electrical Conductivity | 14,2 | 14,20 | <150 | 15,62 | 15,62
Upper Berg: Quality Reserve
The New Template for a quality component of the Reserve
Under these circumstances, site-specific data should be obtained and used to determine more representative local ambient groundwater quality conditions at the site. This Chief Directorate should be notified of such incidences, so as to revise the Reserve accordingly. For example, Iron, Manganese, and pathogens among others.

## Slide 66: Quantitative Water Quality Classes
The software will consider these water quality variables beyond the EC value for water quality
All PSPs will start using all these variables in their assignments beyond the EC value
The software will include the value for charge balance for quality assurance of water quality

## Slide 67
Groundwater Reserve Determination Quality Component: The Process to be followed
STEP 1: Identification of the study area [Quaternary catchment]
STEP 2: Sourcing data for the study area [Data collection/data acquisition task]
STEP 3: Soring and coding the collected data [Data cleaning/data processing task]
STEP 4: Analysis of the processed data using descriptive statistics [Data analysis task]
STEP 5: Assessing water quality class per variable
STEP 6: Assessing water quality class per study area
STEP 7: Determination of the reserve limits
Details under each step are provided in the upcoming report. Today’s presentation is for progress made so far and the wayforward

## Slide 68: Discussion for input on the quality component of the reserve the use of water quality guideline

## Slide 69: GDRM methodology: Progress update
GRDM RQOs: Setting RQOs: Practical session: 15:00-15:45 [45 Minutes]: The New Template

## Slide 70
Water Quality Parameter | Recommended Numerical Limits | Recommended compliance per period | Keynote
pH (upper limit) | 8.40 | 95% | The parameter is considered as a general indicator of water quality in domestic water use
pH (lower limit) | 5.80 | 95% | The parameter is considered as a general indicator of water quality in domestic water use
Electrical conductivity (EC) | 4938.00 | 95% | The parameter is considered as a general indicator of water quality in domestic water use
Calcium (Ca) | 197.60 | 85% | The parameter may commonly be present at concentration of aesthetic or economic concern in domestic water use
Magnesium (Mg) | 304.50 | 85% | The parameter may commonly be present at concentration of aesthetic or economic concern in domestic water use
Sodium (Na) | 5887.80 | 85% | The parameter may commonly be present at concentration of aesthetic or economic concern in domestic water use
Chloride (Cl) | 2040.00 | 75% | The parameter is commonly present at a concentration which may lead to health problems in domestic water use
Sulphate (SO4) | 10.30 | 75% | The parameter is commonly present at a concentration which may lead to health problems in domestic water use
Fluoride (F) | 0.14 | 75% | The parameter is commonly present at a concentration which may lead to health problems in domestic water use
GRDM RQOs: Setting RQOs: Practical session: 15:00-15:45 [45 Minutes]: The New Template

## Slide 71
Discussion for input on the use of Concentration Duration Curves to set RQOs and not using the water quality guidelines
Discussion for input on data for Concentration Duration Curves to set RQOs and not using the water quality guidelines
Discussion for input on analysis of Concentration Duration Curves to set RQOs and not using the water quality guidelines

## Slide 73
Class I Natural
Human activity has caused no or minimal changes to the historical natural structure and functioning of biological communities (animals and plants), hydrological characteristics or the bed, banks and channel of the resource (ecological category A); This is qualitative classification which we are updating
Class II Moderately used/impacted
Resources that are slightly or moderately altered from their natural condition due to the impacts of human activity and water use; retain a high degree of ecological function and integrity (ecological category B to high C); [We are quantifying human activities for quantitative classification of WR]
Class III Heavily used/impacted
Resources that are significantly changed from the Natural class reference conditions due to the impacts of human activity and water use but are nevertheless ecologically sustainable; where there are pressing social and economic reasons to permit uses that will cause limited, short-term and reversible degradation of the resource, cases will be considered on their merits within the framework of long-term sustainability; [We are quantifying human activities for quantitative classification of WR]

## Slide 74
The procedure to determine classes of water resources follow 7 steps:
Step 1: Delineate the units of analysis and describe the status quo of the water resource or water resources.
Step 2: Link the socio-economic and ecological value and condition of the water resource or water resources.
Step 3: Quantify the ecological water requirements and changes in non-water quality ecosystem goods, services and, attributes.
Step 4: Determine an ecologically sustainable base configuration scenario.
Step 5: Evaluate scenarios within the integrated water resource management process.
Step 6: Evaluate the scenarios with stakeholders.
Step 7: Gazette and implement the class configuration.

## Slide 75
The Berg River catchment forms the heart of the WCWSS, which also receives transfers from Theewaterskloof Dam on the Riviersonderend River and Rockview Dam in the Palmiet catchment. Other significant Dams in the WCWSS are the Upper and Lower Steenbras Dams, Berg River Dam, Wemmershoek Dam and Voëlvlei Dam. During winter - the wet season - reverse transfers occur from Berg River Dam to Theewaterskloof Dam.

## Slide 77
Recharge value for local recharge and regional recharge is not clarified. That lack of clarification has
implications when choosing methods and data for estimating recharge. Making decisions on such values on groundwater availability for water allocation and water, protection can be impaired.
Recharge in a mountainous region will recharge in coastal aquifers i.e. rising water levels [Regional flow system]
Recharge in a coastal region will recharge in coastal shallow aquifers .i.e rising water levels [Local flow system]
Recharge variable at quaternary scale versus aquifer scale and boreholes depths in that quaternary catchment: Aquifer scale approach

## Slide 78: Thank you for your attention